## Slide 1
AI-Assisted Recipe Generation
Corrugated carton inspection using CAD/spec PDF, artwork PDF, calibrated camera image and AI-created inspection rules
CAD / DWG / PDF
AI recipe generator
Runtime inspection
Pass / Fail report
Inspection Recipe
slot_top_01 → slot tool
crease_02 → line tool
barcode_03 → match tool
AI
Less manual setup, Use review only

## Slide 2
Why a recipe is needed
Corrugated challenge
PDF/CAD contains lines, text, dimension arrows and artwork mixed together
Software must know which feature is slot, crease, cut edge or print ROI
Without a recipe, runtime algorithm can detect shapes but cannot assign meaning
Solution: Create an AI-assisted Recipe Generator that converts CAD/artwork into measurement rules.

## Slide 3
Two-mode software architecture
Template setup is AI-assisted; runtime inspection is fully automatic after recipe approval.
1
Load CAD/spec PDF + artwork PDF
2
AI generates draft inspection recipe
3
Engineer reviews only exceptions
4
Save approved recipe per template
5
Runtime camera inspection
Setup Mode
Run once per new carton design
AI extracts features and dimensions
Engineer approves generated recipe
Recipe Database
Template ID and version
Feature type and ROI
Expected dimension, tolerance, detector
Runtime Mode
Select job/template
Capture, register and inspect automatically
Report deviations and failures

## Slide 4
AI Recipe Generator: detailed approach
Use a hybrid system: deterministic parsing where possible, AI classification where understanding is required.
1
PDF/DWG/DXF parser extracts vectors, text and rendered images
2
Layout AI classifies features: slot, crease, cut, panel, dimension text
3
Artwork AI detects barcode, logo, symbols, text blocks and ROIs
4
Geometry reasoning links dimensions to features
5
Structured recipe JSON is created automatically
Why hybrid is better than a single black-box model
PDF geometry and text extraction is deterministic when vectors are available
AI is used for semantic classification and complex layout understanding
Rule logic converts AI detections into measurable inspection instructions
Recipe output
Feature identity: slot / crease / label / barcode
Expected coordinates and dimensions in inch/mm
Measurement method and tolerance per feature

## Slide 5
CAD structural extraction: from lines to carton features
The AI does not only detect a line; it assigns meaning and creates a measurement rule.
Detected CAD element
AI classification
Generated inspection rule
Outer contour polyline
Blank boundary
Measure overall length, width, skew, edge deviation
Vertical/horizontal internal line
Crease / score line
Search local ROI, fit line, compare X/Y position
Cut opening at edge
Slot
Measure slot depth, slot width/gap and offset
Panel partition lines
Panel / flap boundary
Measure panel width and flap height
Dimension text + arrows
Expected value
Link dimension value to nearby feature
Example: vertical line at X = 5.14” → crease_01 expected_x = 5.14 inch

## Slide 6
Artwork extraction: from PDF artwork to inspection ROIs
The artwork PDF is converted into expected print objects with type, position, size and inspection method.
1
Render artwork PDF at high DPI
2
AI detects print objects
3
Assign object type and expected box
4
Create ROI inspection rules
Detected print types
Barcode / QR
Logo / product mark
Text block / warnings
Symbols and certification icons
Stored per ROI
Expected X/Y, width, height
Orientation and local tolerance
Master patch or barcode pattern
Required / optional flag
Runtime check
Search near expected location
Measure X/Y shift and rotation
Check present, missing or wrong
Confidence + pass/fail

## Slide 7
How AI knows which slot or crease has which dimension
Dimension-to-feature linking is handled by geometry reasoning, not by runtime guessing.
1. Read dimension evidence
Text: 7.02”, 4.06”, 5.15”
Dimension arrows and extension lines
Nearby feature lines or slot geometry
2. Build geometry graph
Nodes: lines, slots, arrows, text
Edges: near, parallel, perpendicular, bounded by
Inference: this text belongs to this measured feature
Example relationship:
slot opening is bounded by top edge and bottom cut line; dimension arrow spans same direction.
3. Write recipe rule
Feature name and type
Expected value in inch/mm
Reference edge or coordinate
Measurement rule and tolerance
slot_top_01:
type = slot
reference = top_edge
expected_depth = 5.9375 in

## Slide 8
Inspection recipe: output of AI setup
This structured file tells runtime exactly what each feature is, where to search and how to measure.
Recipe contents
Template ID, unit, version and tolerance profile
Sheet coordinate system and reference edges
Structural features: boundary, crease, slot, panel, flap
Artwork features: barcode, logo, text block, symbol
For each feature: ROI, expected value, detector, pass/fail rule
Example recipe fragment
{
"template_id": "306694",
"unit": "inch",
"features": [
{"name":"slot_top_01",
"type":"slot",
"roi":[1.0,0.0,15.0,6.5],
"expected_depth":5.9375,
"detector":"slot_depth_tool",
"tolerance":0.15},
{"name":"barcode_panel_1",
"type":"barcode",
"expected_box":[10.2,28.4,4.0,0.8],
"detector":"barcode_position_tool",
"tolerance":0.15}
]
}

## Slide 9
Image acquisition and calibration strategy
Detailed solution
Corrugated Carton Vision Inspection
Capture setup
• Fixed camera height and angle
• Complete 70” × 40” field coverage
• Uniform non-reflective lighting
• Flat background and repeatable sheet placement
• High sharpness, low motion blur
Calibration pipeline
• Lens distortion correction
• Perspective correction using corner/fiducial markers
• Pixel-to-inch mapping
• Sheet rotation and scale normalization
• Periodic calibration verification
Accuracy controls
• Sub-pixel line fitting for edges
• Reference marker quality checks
• Reject image if sheet is cropped or blurred
• Measurement repeatability test with known gauge/ruler
• Separate POC accuracy from production accuracy
Target: ±0.1” to ±0.2” only after calibration is validated

## Slide 10
Runtime inspection: recipe-driven, not blind detection
Once the recipe exists, every captured sheet is inspected automatically using the correct tool per feature.
1
Capture real carton sheet image
2
Detect boundary / markers and register image
3
Project recipe ROIs onto captured image
4
Run type-specific detector in each ROI
5
Compare actual vs expected
Example: slot
ROI is known from recipe
Detect top cut, side cuts and slot bottom
Measure depth from reference edge
Compare with expected 5.75 in
Example: crease
Search local crease ROI
Enhance low-contrast line
Fit crease line
Compare X/Y or angle error
Example: artwork
Search only near expected location
Template/barcode/object matching
Measure shift and rotation
Report missing/wrong print

## Slide 11
Feature-specific detector library
Different carton features need different inspection tools; the recipe selects the correct one.
Feature type
Detector / algorithm
Output measurement
Boundary / cut edge
Contour + line fitting + sub-pixel edge refinement
Length, width, skew, edge deviation
Crease / score line
Local contrast enhancement + LSD/Hough + line fitting
Position error, angle error, presence/absence
Slot / gap
Edge grouping + contour fitting inside slot ROI
Depth, gap width, offset from reference edge
Panel / flap
Distance between detected structural lines
Panel width, flap height, cumulative error
Barcode / logo / text block
Barcode detector, template matching, feature matching, optional OCR
Presence, X/Y shift, rotation, match score
The AI-generated recipe reduces ambiguity: a crease ROI will never be processed like a barcode, and a slot ROI will never be treated as random artwork.

## Slide 12
Comparison logic: expected vs actual
All outputs become measurable deviations in inch/mm and pass/fail decisions.
Dimension example
CAD length = 57.125 in
Detected = 57.020 in
Error = -0.105 in
Tolerance = ±0.200 in
Result = PASS
Same formula is used for width, panel size, slot depth and crease position.
Position example
Expected barcode:
X=10.20, Y=28.40
Detected barcode:
X=10.45, Y=28.30
X error=+0.25
Y error=-0.10
Tolerance=±0.15 → FAIL
Decision output
Actual value
Expected value
Deviation
Tolerance
Pass / fail
Annotated failure location

## Slide 13
Technical risks and mitigation
The proposal should be credible: AI reduces setup effort, but robust validation and review are still required.
Risk
Impact
Mitigation
Scanned/non-vector PDFs
Low-quality geometry extraction
Render + vision extraction; request DXF/DWG where available
Cut and crease lines look similar
Wrong feature classification
AI confidence score + engineer approval for uncertain features
Dimension text linked to wrong feature
Incorrect measurement rule
Geometry graph validation and overlay review
Low-contrast crease in camera image
Missed crease detection
Directional/side lighting and local contrast detectors
Large 70×40 in FOV with tight tolerance
Measurement error due to calibration/perspective
Lens calibration, fixed mount, reference markers, homography validation
Artwork varies by print process
False mismatch
Use tolerance windows and confidence thresholds; avoid color-quality claims in Phase 1